## Slide 1: Power Factor Prediction
Prepared By: Bhumik P Shah

## Slide 2: Conceptual Background of Power Factor
The power factor is the cosine of the phase difference between voltage and current, and as a result, the power factor is measured using the formula Power Factor = cosɸ, where ɸ is the phase difference between the voltage and current phasor.
The power factor values lies in the range of 0 to 1.
Power Factor= Active Power/Apparent Power as per power triangle.
As per the ideal condition the power factor should be closer to 1 i.e is unity.
Generally, a power factor of 0.9 or above is considered as a good power factor.

## Slide 3: Few Important concepts related to power sector
The generating station generates electricity with a voltage level in the range of 11kV to 25kV depending on the alternator(generator) size and ratings.
The voltage level is increase to 132 kV/220kV/400kV using power transformers(step up) in the generating substations.
The higher the voltage better it is as transmission and distribution loss would be minuscule at higher voltage.
At higher voltage, volume of conductor is reduced. Area of conductor A ∝ 1/Vs² Where Vs = supply voltage .
So that material requirement is reduced and hence cost of the material and transmission is reduced.

## Slide 4: Assumptions made
The given data is considered for 400kV Transmission line looking at the line current/ Maximum Demand Profile.
It is assumed that a bundle conductor is used in the transmission line having a power carrying capacity of 600 to 650 MW.

## Slide 5: Independent features in dataset
VL1,VL2,VL3: Phase voltage of line1,line2 and line 3 in kV.
IL1,IL2,IL3:Line current for line1, line2 and line3 in Ampere(A).
VL12,VL23,VL31: Line voltage between line 1 and line 2, line 2 and line 3 and line 3 and line1.
INUT: Current flowing in neutral wire in Ampere(A).
PFL2,PFL3, Avg_pf,: Power factor of line 2, line 2 and average power factor of three lines.
Sum_PF: Sum of power factor.
FRQ: Frequency of the system in Hertz(HZ).
THDVL1,THDVL2 and THDVL3: Total Harmonic distortion in percentage i.e voltage distortion for line1,line 2 and line 3 in decibels(dB).
THDIL1,THDIL2 and THDIL3: Total Harmonic distortion in percentage i.e current distortion for line1,line 2 and line 3 in decibels(dB).
MDIL1,MDIL2 and MDIL3: Maximum Demand in MVA for line 1 ,line 2 and line 3.

## Slide 6: Dependent Features
PLF1: Power factor of line1
As the target variable PFL1 is continuous is nature it is a Regression problem.

## Slide 7: Libraries used
Numpy
Pandas
scikit-learn
Scipy
Seaborn
Matplotlib
Joblib

## Slide 8: Data Preprocessing
The dataset is having 19308 records and 25 features after dropping null/Missing values from the dataset.
By using describe method of pandas it is observed that the features VL1, VL2, VL3,VL12,VL23 and VL31 are having left tailed skewness as median is greater than mean and the same has been confirmed using distplot.
The features IL1,IL2, IL3,INUT are having right tailed skewness as mean is greater than median and the same has been confirmed using distplot.
There is a huge difference between 75% quantile and max values for features IL1,IL2 and IL3 which says outliers are present in those features.

## Slide 9: Types of faults in electrical power system
L-G(line to ground) fault is the most common fault in electrical power system with 65-70 % percent of faults are of this type.
15 to 20% of faults are of double line to ground fault.
Triple line to ground fault is a rare type of fault existing in electrical power system.

## Slide 10: Abnormality observed in phase and line voltage.
Some of the records are having value as zero in features VL1,VL2 ,VL3(phase voltage)and VL12,VL23,VL34(line to line voltage) which says either the transmission line is under forced outage due to faults or it can be due to the shutdown taken for periodic maintenance of line as during normal operating conditions these parameters can never be zero.
The permissible limit of voltage variations allowed in EHV line is in the range of -12.5 to 10.5 and anything beyond that is not acceptable as the protection system(relays and breakers) will operate and trip the line for voltage beyond permissible limit .
There are 1730 records in VL12 having value as zero. The feature VL12 can never have zero value (line to line voltage)for healthy power system that too when other parameters of the line like current and voltage(VL23 & VL13) are having values within the acceptable range.

## Slide 11: Abnormality observed in line current
Some of the records are having value as zero in features IL1,IL2 and IL3(line current) which says there is a mismatch between generation and demand and such type of situations hardly exist.
Second scenario can be there is an open circuit which implies the conductor used for carrying current is broken from somewhere resulting into features IL1, IL2 and IL3 values as zero.

## Slide 12: Harmonics
In an electric power system, a harmonic of a voltage or current waveform is a sinusoidal wave whose frequency is an integer multiple of the fundamental frequency.
They are a frequent cause of power quality problems and can result in increased equipment and conductor heating and can damage it.
Harmonic frequencies are produced by the action of non-linear loads such as rectifiers, discharge lighting, computer, diode, bulbs or saturated electric machines.

## Slide 13: Total Harmonic Voltage and current Distortion
THD, of a signal is a measurement of the harmonic distortion present and is defined as the ratio of the sum of the power of all harmonic components to the power of the fundamental frequency.
It can be expressed in percentage or decibel , lesser the value better it is .
Allowed permissible limit for THD specifically for voltage is 1.5 to 3% and for current it is 8 to 10 % and anything about that is abnormal or dangerous.
The abnormality is observed in 339 records where THDVL1(Voltage distortion) is exceeding the permissible limit which is dangerous for the power system .

## Slide 14: Maximum Demand(loading)
The main objective of power system is that the sending end voltage should be equal to receiving end voltage and that is governed by surge impedance loading in other words it is nothing but a safe loading of a transmission line.
The transmission line has two components inductor in series and shunt capacitor in parallel. The inductor is said to be absorber of reactive power and shunt capacitor is said to generator of reactive power.
The amount of reactive power generated by capacitor should be absorbed by series inductor which is an ideal situation.
The abnormalities is observed in 3450 records for feature MDIL1 where the maximum demand is less than 100 MVA which says the transmission line is lightly loaded resulting into voltage at receiving end greater than sending end voltage.

## Slide 15: Outliers detection and Treatment
Data Visualization is the graphical representation of the information and data. Further, by using visual elements like charts, graphs and maps data visualization tools provide an accessible way to see and understand trends, outliers and patterns in data.
The outlier detection is carried out using boxplot and distribution plot .
The outliers are treated using IQR(Inter Quartile Range) method for features VL1, VL2, VL3, IL1, IL2, IL3, VL12, VL23, VL31,THDVL1,THDVL2,THDVL3, THDIL1, THDIL2 and THDIL3 instead of removing them using Zscore ,as removing the outliers will create data loss which should be avoided as data is vital and costly.

## Slide 16: Skewness
Skewness is the degree of distortion from a normal distribution.
If the values of a certain independent variables (features) are skewed, depending on the model, skewness may violate model assumptions or may impair the interpretation of feature importance.
All the numerical features i.e independent features in these dataset are having skewness greater than 0.5 which has to be treated as the skewed data will hamper model performance and accuracy.
There are different methods to treat skewness 1) power transform 2) Cube root transformation 3)square root transformation 4)log transformation 5)Box cox Transformation.
Power Transform method is applied for this dataset and all those features with skewness greater than 0.5 is treated.

## Slide 17: Correlation
Correlation is an indication about the changes between two variables.
As per the heatmap it can be said that the target/label attribute PFL1 is having positive linear correlation with Avg_pf.
The features FRQ, THDIL2, THDIL3,THDIL1 are having less(negative) correlation with target/label PFL1.

## Slide 18: Model Building
Standard Scaling is applied first before splitting the data into train_test_split.
The various algorithms like Linear Regression, Decision Tree Regressor, SVR, K Neighbors Regressor, Ada Boost Regressor, Gradient Boosting Regressor, Random Forest Regressor, Lasso , Ridge are used.
First approach is to find r2 score using all mentioned algorithms and finding the best model amongst it.
The cross validation is carried out for all the mentioned algorithms to help us find the best model.

## Slide 19: Hyper Parameter Tuning
Say for example linear Regression, Decision Tree Regressor and Gradient Boosting Regressor are having same values i.e minimum difference between cross_val_Score and r2_score.
. To find the best models amongst these can be done using Hyper tuning where the parameters are tuned to get better r2_score as compared to the one’s without tuning.
Decision tree Regresor is my best model with r2 score of 91% as per assumption made.

## Slide 20
Thank You